## Slide 1
Temperature Controller – TC3051
The Meadowlark Optics TC3051 is a single channel, microprocessor based temperature controller specifically designed to work with Meadowlark Optics’ liquid crystal devices equipped with the Temperature Sensing and Control (TSC) option.
The TC3051 requires minimal setup:
1. Connect the included power supply.
2. Connect the temperature control cable to both the TC3051 and the liquid crystal device.
3. Turn the power on.
Stand Alone
LED Display
1 Channel Temperature Control
Key Features
• • •
SPECIFICATIONS | 
Requirements | 100 – 240V ac, 47 – 63 Hz, 500 mA
Fuse | Internal (not user serviceable)
Environment | 0˚C to + 50˚C (Operating) -55˚C to + 100˚C (Storage)
External Dimensions (W x D x H) | 5.08 x 5.25 x 1.50 in. (12.90 x 13.33 x 3.81 cm)
Weight | lb. (0.45 kg)
Temperature Readout Resolution | 1˚C
Temperature Readout Range | 0˚C to 99˚C
Setpoint Resolution | 1˚C
Setpoint Range | 20˚C to 60˚C
ORDERING INFORMATION | 
Temperature Controller | TC3051
Liquid Crystal Suite
• • •
Variable Retarders
Liquid Crystal Variable Retarder
UV Variable Retarder
MWIR Variable Retarder
OEM LCVR
Rotators
Achromatic High Speed Rotator
Binary Rotator
Polarization Rotator
Shutters / Attenuators
Achromatic High Speed Shutter
High Contrast Shutter
Variable Attenuator
Controllers
Analog Controller
FLC Controller
LC Digital Interface Controller
Temperature Controller
Two Channel High Voltage Controller